## Slide 1
ID
IEEE SISY 2026 · 24TH INT'L SYMP. ON INTELLIGENT SYSTEMS & INFORMATICS · PULA
Real-Time Training-Free Multimodal
Identity Verification using Biometric
Temporal Score Fusion
Antonio Labinjan · Nikola Tanković
Faculty of Informatics, Juraj Dobrila University of Pula
01
Notes: Good morning/afternoon. This talk presents a real-time, training-free framework for multimodal identity verification that fuses face and voice biometrics. The core idea: get the robustness benefits of multimodal fusion without paired training data or a joint fusion network.

## Slide 2
THE PROBLEM
Unimodal Biometrics Fail in the Real World
F
Face Recognition
● Sensitive to illumination changes
● Degrades under pose variation
● Fails on motion blur & occlusion
V
Voice Verification
● Degrades under ambient noise
● Struggles with reverberant rooms
● Vulnerable to cross-speaker confusion
Result: elevated false rejection and false acceptance rates in deployment
02
Notes: Unimodal biometrics degrade in the wild. Face recognition is sensitive to illumination, pose, and blur; voice verification degrades under noise and reverberation. Both effects push false rejection and false acceptance rates up, which motivates combining modalities.

## Slide 3
MOTIVATION
The Gap in Existing Multimodal Fusion
Paired
Dataset
Joint
Training
Fused
Model
✕
→ Deep multimodal fusion needs synchronized, paired datasets
→ Joint training adds computational overhead and overfitting risk
→ Prevents independent upgrades of face / voice sub-models
03
Notes: Most deep multimodal fusion methods need synchronized, paired audio-visual datasets and joint training. That adds computational overhead, risks overfitting, and locks the face and voice sub-models together — you can't upgrade one independently. This is the gap we address.

## Slide 4
THIS PAPER
Our Contributions
1
Real-time multimodal framework fusing face and voice biometrics
2
Unified Qdrant retrieval backend for heterogeneous embeddings
3
Training-free fusion — no joint optimization or paired data required
4
Temporal decision layer: agreement, missing-stream, and conflict states
5
Offline evaluation quantifying the accuracy / security trade-off
04
Notes: Five contributions: a real-time face+voice framework; a unified Qdrant retrieval backend across heterogeneous embedding spaces; a training-free fusion mechanism; an explicit temporal decision layer with agreement/missing/conflict states; and an offline evaluation quantifying the accuracy-security trade-off.

## Slide 5
SYSTEM DESIGN
System Architecture Overview
Camera Node
Microphone Node
CLIP ViT-B/32
512-D face embedding
VoiceNet CNN
128-D speaker embedding
Unified Vector DB (Qdrant)
cosine search · shared identity metadata
State Logic Engine → Identity Verification Output
05
Temporal Stream Aligner
peak match (Cᵥ, Cₐ) per identity, before state logic
Notes: Here is the full pipeline. Camera and microphone streams are processed by independent encoders into face and voice embeddings. Both are queried against a shared Qdrant backend. The temporal stream aligner takes the peak match per modality, and the state logic engine turns that into a final identity decision. Walk left to right — this is the mental model for the rest of the talk.

## Slide 6
VISUAL PIPELINE
Face Recognition Pipeline
Face Image
224×224
CLIP ViT-B/32
(openai/clip-vit-base-patch32)
512-D
Embedding
Qdrant
Visual Index
→ Builds on prior zero-shot work (Labinjan et al.) — encoder unchanged
→ Robust to domain shifts: pose, illumination, and blur variation
→ Migrated retrieval backend from FAISS → Qdrant for unified infrastructure
06
Notes: The visual pipeline reuses the CLIP ViT-B/32 vision backbone from our prior zero-shot face recognition work, unchanged. It takes normalized 224×224 face frames and outputs 512-D embeddings that are robust to pose, illumination, and blur. The only architectural change here is the retrieval backend — migrated from FAISS to Qdrant to align with the auditory pipeline.

## Slide 7
AUDITORY PIPELINE
Voice Verification Pipeline
Audio Chunk
(mono)
Log-Mel
Spectrogram
VoiceNet CNN
5 conv blocks · 32→256 ch
128-D
Embedding
→ Trained closed-set on VoxCeleb: Conv2D + BatchNorm + ReLU + MaxPool ×5
→ The "truncation trick": Softmax head used only for training, then discarded
→ Remaining backbone reused zero-shot as an open-set speaker embedding extractor
07
Notes: Voice verification uses a custom convolutional network, VoiceNetEmbedding, trained on VoxCeleb. Five conv blocks expand channels from 32 to 256 over log-Mel spectrograms. Note the 'truncation trick': we train with a closed-set softmax head, then discard it after convergence and reuse only the backbone as a zero-shot, open-set embedding extractor — 128-D output.

## Slide 8
INFRASTRUCTURE
Why Unify on Qdrant?
Two Separate FAISS Indexes
✕ Two vector indexes to maintain
✕ Duplicated identity metadata
✕ Manual sync across storage layers
✕ Separate persistence mechanisms
One Unified Qdrant Backend
✓ Centralized vector storage & retrieval
✓ Shared identity + metadata schema
✓ Modality-specific similarity retained
✓ One deployment configuration
Clarification: Qdrant unifies infrastructure and identity metadata — not the vector spaces themselves. Face (512-D) and voice (128-D) embeddings remain separate.
08
Notes: A common misconception to head off: Qdrant does not merge face and voice vectors into one space — 512-D and 128-D vectors are structurally incompatible. What it unifies is the infrastructure: one identity schema, one metadata layer, one deployment, instead of two separate FAISS indexes with duplicated metadata and manual sync.

## Slide 9
METHODOLOGY
Score Alignment & Normalization
Camera and microphone streams arrive asynchronously at different rates — strict frame-level alignment is infeasible. Instead, the system takes the peak similarity score per modality within an evaluation window.
V
Visual peak score
SV = max{ sv1, sv2, …, svn }
A
Auditory peak score
SA = max{ sa1, sa2, …, sam }
Eq. (1)–(2): both pathways share Qdrant cosine-similarity retrieval, so Sᵥ and Sₐ are compatible and can be thresholded before fusion.
09
Notes: Camera and microphone streams arrive asynchronously at different rates, so strict frame-level alignment isn't practical. Instead we take the peak similarity score per modality within an evaluation window — S_V and S_A. Because both pathways share the same Qdrant cosine-similarity configuration, these peak scores are directly comparable and can be thresholded before fusion.

## Slide 10
CORE CONTRIBUTION
Temporal Fusion Logic — Decision States
CONFIRMED
Both modalities agree on identity → harmonic-mean fused score
VISION_ONLY
Voice missing / rejected → fall back to visual score alone
AUDIO_ONLY
Face missing / rejected → fall back to voice score alone
CONFLICT
Modalities disagree on identity → suppressed, rejected
Harmonic-mean fusion under CONFIRMED
Sfused = 2 · SV · SA / (SV + SA + ε)
10
Notes: This is the core novelty — spend extra time here. Four explicit states: CONFIRMED when both modalities agree, in which case we combine scores with the harmonic mean, which penalizes a weak match in either modality rather than just averaging. VISION_ONLY or AUDIO_ONLY when one stream is missing or rejected. And CONFLICT — the safety mechanism — when the two modalities disagree on identity; in that case, the decision is suppressed and the probe is rejected rather than risking a false accept.

## Slide 11
EXPERIMENTAL SETUP
Dataset & Evaluation Protocol
known_data/
identity_i/
train/ (enrollment gallery)
audio/
vision/
val/ (evaluation probes)
audio/
vision/
Three probe outcomes
Correct identification
prediction matches ground truth
Misidentification
system accepts a wrong identity
Rejection
outputs UNKNOWN or CONFLICT
11
Notes: Briefly: evaluation uses an identity-centric directory structure. Each identity has a train/ split for enrollment and a val/ split of unseen probes, each further split into audio and vision. Every probe trial ends in one of three outcomes: correct identification, misidentification, or rejection.

## Slide 12
METHODOLOGY
Evaluation Metrics
Accuracy
Ncorrect / N
Misidentification Rate
Nmisid / N
Rejection Rate
Nreject / N
Together, the three quantities describe complementary failure behavior across the unimodal and fused configurations.
12
Notes: Three metrics, precisely defined: accuracy is correct identifications over total; misidentification rate is the fraction of probes accepted under the wrong identity — this is the dangerous failure mode; rejection rate is the fraction the system declines to confirm. Keep these in mind — the results slide depends on distinguishing misidentification from rejection.

## Slide 13
RESULTS
Unimodal vs. Fused Performance
Configuration | Accuracy | Misident. Rate | Reject. Rate
Face-only | 92.00% | 0.00% | 8.00%
Voice-only | 83.00% | 9.00% | 7.00%
Fused | 75.00% | 0.00% | 25.00%
9.00% → 0.00%
misidentification rate, voice-only → fused
Rejection rate rises to 25% — the deliberate cost of a security-first design.
Trade-off framing: accuracy drops from 92% to 75%, but misidentification — the dangerous failure mode — falls to zero by increasing rejection under cross-modal contradiction.
13
Notes: Face-only reaches 92% accuracy with zero misidentifications, but an 8% rejection rate. Voice-only is weaker: 83% accuracy but a 9% misidentification rate. The fused system trades accuracy down to 75% — with rejection rate rising to 25% — in exchange for driving misidentification to 0%. This is a deliberate design choice: in a security-oriented verification setting, refusing a legitimate user is a much cheaper mistake than accepting an impostor.

## Slide 14
ANALYSIS
Why It Works: Complementary Error Patterns
Face-only errors: sparse
Errors mostly appear as rejections under pose, scale, or quality variation — rarely cross-identity.
Voice-only errors: scattered
Errors scatter across multiple enrolled identities — the acoustic subsystem confuses speakers.
Non-overlapping failure modes: when audio misidentifies, vision usually gives the correct match or UNKNOWN — so the CONFLICT state catches the contradiction.
14
Correct-identity error (rejection)
Cross-identity misidentification
Notes: This is the mechanism behind that result. Face-only errors are sparse and mostly manifest as rejections under pose, scale, or quality variation — rarely as a wrong identity. Voice-only errors scatter across many enrolled identities — the acoustic subsystem is more prone to cross-speaker confusion. Because these failure modes rarely overlap, when voice misidentifies, vision usually still gives the correct match or an unknown — so the CONFLICT state catches the contradiction and suppresses the unsafe accept.

## Slide 15
CONCLUSION & FUTURE WORK
Training-Free Fusion, Security-First Results
What We Did
✓ Training-free — no paired audio-visual data
✓ No fusion network to optimize
✓ Misidentification cut from 9.00% → 0.00%
What's Next
→ Edge-device deployment
→ Latency & resource profiling
→ Live cross-modal synchronization
Thank you — questions welcome
antonio.labinjan@unipu.hr · nikola.tankovic@unipu.hr
15
Notes: To summarize: a training-free multimodal verification framework needing no paired audio-visual data and no fusion network to train, which cut misidentification from 9% to 0% at the cost of a higher rejection rate — an explicit, tunable trade-off rather than an incidental one. Future work: benchmarking on edge hardware, profiling latency and resource use, and handling live cross-modal synchronization instead of the offline peak-score aggregation used here. Thank you — happy to take questions.